Computer Networks

Lab 11

Hamza Shahid
20P-0117
BSSE-5A

Task 01:

Device	Interface	IP Address	Subnet Mask	Default Gateway
R1	G0/0	192.168.100.1	255.255.255.224	N/A
	G0/1	192.168.100.33	255.255.255.224	N/A
	S0/0/0	192.168.100.129	255.255.255.224	N/A
R2	G0/0	192.168.100.65	255.255.255.224	N/A
	G0/1	192.168.100.97	255.255.255.224	N/A
	S0/0/0	192.168.100.158	255.255.255.224	N/A
S1	VLAN 1	192.168.100.2	255.255.255.224	192.168.100.1
S2	VLAN 1	192.168.100.34	255.255.255.224	192.168.100.33
S3	VLAN 1	192.168.100.66	255.255.255.224	192.168.100.65
S4	VLAN 1	192.168.100.98	255.255.255.224	192.168.100.97
PC1	NIC	192.168.100.30	255.255.255.224	192.168.100.1
PC2	NIC	192.168.100.62	255.255.255.224	192.168.100.33
PC3	NIC	192.168.100.94	255.255.255.224	192.168.100.65
PC4	NIC	192.168.100.126	255.255.255.224	192.168.100.97

Connectivity verification:
It become very easy when you made table and then all you have to do is just to demonstrate topology.

Steps:
Assign IPs, subnet mask and default gateway to all the PCs as we have done before (by followinng the table).

- Then assign IP and default gateway to the switches.

- Then configure the routers.

Based on the topology, how many subnets are needed?
Ans: 5

How many bits must be borrowed to support the number of subnets in the topology?
Ans: 2^3 must be borrowed which is: 8 (cz 5 subnets are needed)
First and last will not be used.
By going through table, we need 3 bits.

How many subnets does this create?
Ans: 2^3 = 8

How many usable hosts does this create per subnet?
Ans: 2^5 – 2 = 30

Calculate the binary value for the first five subnets. The first two subnets have been done for you.
Ans:

Subnet	Network / Address	Bit 7	Bit 6	Bit 5	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
0	192.168.100.	0	0	0	0	0	0	0	0
1	192.168.100.	0	0	1	0	0	0	0	0
2	192.168.100.	0	1	0	0	0	0	0	0
3	192.168.100.	0	1	1	0	0	0	0	0
4	192.168.100.	1	0	0	0	0	0	0	0

   6. Calculate the binary and decimal value of the new subnet	mask.
We borrowed 3 bits, so we have to put 1 at 1st 3 places of last binary octet of subnnet mask

First / Octet	Second / Octet	Third / Octet	Mask / Bit 7	Mask / Bit 6	Mask / Bit 5	Mask / Bit 4	Mask / Bit 3	Mask / Bit 2	Mask / Bit 1	Mask / Bit 0
11111111	11111111	11111111	1	1	1	0	0	0	0	0

Decimal Value: 255.255.255.224

Subnet Table:

Subnet Number	Subnet Address	First Usable Host Address	Last Usable Host Address	Broadcast Address
0	192.168.100.0	192.168.100.1	192.168.100.30	192.168.100.31
1	192.168.100.32	192.168.100.33	192.168.100.62	192.168.100.63
2	192.168.100.64	192.168.100.65	192.168.100.94	192.168.100.95
3	192.168.100.96	192.168.100.97	192.168.100.126	192.168.100.127
4	192.168.100.128	192.168.100.129	192.168.100.158	192.168.100.159
5	192.168.100.160	192.168.100.161	192.168.100.190	192.168.100.191
6	192.168.100.192	192.168.100.193	192.168.100.222	192.168.100.223
7	192.168.100.224	192.168.100.225	192.168.100.254	192.168.100.255

Step 2: Assign the subnets to the network shown in the topology.

1. Assign Subnet 0 to the LAN connected to the GigabitEthernet 0/0 interface of R1:
  192.168.100.0 /27
2. Assign Subnet 1 to the LAN connected to the GigabitEthernet 0/1 interface of R1:
  192.168.100.32 /27
3. Assign Subnet 2 to the LAN connected to the GigabitEthernet 0/0 interface of R2:
  192.168.100.64 /27
4. Assign Subnet 3 to the LAN connected to the GigabitEthernet 0/1 interface of R2:
  192.168.100.96 /27
5. Assign Subnet 4 to the WAN link between R1 to R2:
  192.168.100.128 /27